## Slide 1
634
586
562
538

## Slide 2: Standard Cells Do Matter: Uncovering Hidden Connections for High-Quality Macro Placement
DATE 2024

## Slide 3: Introduction
Dataflow defines the moving of data between the macros and standard cells and influences the timing and power consumption of the circuit.
By minimizing the data movement, the placement of macros can reduce the overall design cost, as it reduces the routing process complexity and required interconnects number eventually.

## Slide 4: Introduction
Though Reinforcement Learning (RL) or Deep Learning (DL)-based methods such as [1]–[4] have been proposed to offer benefit of automating the macro placement actions, they incurred legalization problems, huge computational, and the training design dataset is not easy to access.
Dataflow-aware macro placers [5]–[10], where the dataflow is analyzed and used as constraints for further placement of the macros.

## Slide 5: Introduction
In [5], optimized data path layout was generated by utilizing rule information directly extracted from dataflow graphs.
The approach in [7] considered dataflow and utilized the corner stitching data structure to address the problem of preplaced macros, which cannot be handled by simulated annealing (SA).
A recently released macro placer, RTL-MP [8], considered the macro-to-macro dataflow and proved that such dataflow is helpful in getting a human-quality layout.

## Slide 6: Introduction
Although the macro placers have been equipped with some forms of dataflow analysis capability, they mainly expose and utilize the virtual or direct connections among macros (i.e. macro-macro connections).
While an important fact is that standard cells are usually placed in clusters based on their hierarchy. If the cluster is large enough, it can be modeled as a “macro”. Thus the placement of standard cell clusters can in turn impact how macros are placed.

## Slide 7: Introduction
Propose a novel methodology to comprehensively extract all direct and indirect dataflow connections among macro clusters and cell clusters, and use them as an important guidance for macro placement.

## Slide 8: Methodology