## Slide 1: A High Performance Detailed Router Based on Integer Programming with Adaptive Route Guides
ASP-DAC 2024

## Slide 2: Introduction
Facing the high complexity of the detailed routing problem, there are two main approaches to solve it, including sequential routing approach and concurrent routing approach.

## Slide 3: Introduction
The sequential routing approach uses iterative rip-up and reroute (R&R) to reduce the number of design rule violations (DRVs) [1]–[7].
Issue
  The net ordering during routing is critical for the runtime and the solution quality.
  Net routes ripped-up may be discarded too early.

## Slide 4: Introduction
The net ordering issue is considerably mitigated by queue-based R&R approach TritonRoute-WXL[7].

## Slide 5: Queue-based R&R
aggressor and victim
Element : (net name, isRoute, route times)
isRoute = true : (re)route and incremental DRC
false : incremental DRC only

## Slide 6: Queue-based R&R

## Slide 7: Queue-based R&R

## Slide 8: Introduction
The concurrent routing approach formulates detailed routing as integer linear programming (ILP), Boolean satisfiability(SAT), or satisfiability modulo theories (SMT) problems [9]–[11].
In this approach, route construction of multiple nets are performed concurrently to optimize the solution quality.

## Slide 9: Introduction
A well-studied formulation is to treat the assignment of each routing grid point to a net (routing-grid-based) as a decision variable, and model connectivity and design rules as constraints.
It generates high quality solutions, but often requires long runtime. As a result, it is generally applied in small routing regions.
routing-grid-based
Horizontal : 6 X 9 = 54
Vertical : 8 X 7 = 56
54 + 56 = 110 decision variables

## Slide 10: Introduction
Another formulation is to use selection of possible net routes (route-based) as decision variables.
Benefits
  It is more scalable than the routing-grid-based formulation [12].
  Overcome the issue of discarding routes in early R&R procedure.
route-based
netA : rA1 , rA2 => 2
netB : rB1 , rB2 => 2
netC : rC1 => 1 2 +2 + 1 = 5 decision variables

## Slide 11: Introduction
routing-grid-based
Horizontal : 6 X 9 = 54
Vertical : 8 X 7 = 56
54 + 56 = 110 decision variables
route-based
netA : rA1 , rA2 => 2
netB : rB1 , rB2 => 2
netC : rC1 => 1 2 +2 + 1 = 5 decision variables

## Slide 12: Contribution
An effective detailed routing algorithm with a scalable IP formulation is proposed.
High quality candidate routes are generated using queue-based R&R with adaptive global route guides following.
An efficient design rule checking engine which supports examining nets with multiple routes simultaneously is designed.
Achieves better solution quality and shorter runtime than the state of-the-art TritonRoute-WXL [7] results.

## Slide 13: IPAG - Overall Flow
Process in Local Routing Region

## Slide 14: IP Formulation
The detailed routing procedure in each local region include two phases, namely IP instance construction and IP solving to select best routes.

## Slide 15: IP Formulation
preferred direction and non-preferred direction

## Slide 16: IP Formulation
The formulation has some unique properties compared to the routing-grid-based formulation.
  Explicit representation of various design rules in the formulation is not required.
  The size of IP instances depends on the number of nets to be routed and the number of candidate routes.
  The candidate routes are not restricted to be on grid, so it is applicable for both gridded routing and gridless routing.

## Slide 17: Candidate Generation with Adaptive Guide Following
Adaptive Global Routing Guides

## Slide 18: Candidate Generation with Adaptive Guide Following
Queue-based R&R

## Slide 19: Candidate Generation with Adaptive Guide Following
Queue-based R&R

## Slide 20: Multi-Route Design Rule Checking
Treating each candidate route as a net in design rule checking, multiple candidate routes of a net can be processed at the same time.

## Slide 21: Multi-Route Design Rule Checking

## Slide 22: EXPERIMENTS
Use CPLEX[18] as the IP solver.
Use ISPD 2018 detailed routing benchmark suite [19].
The detailed router runs on a computer with an Intel CPU @ 2.30GHz and 64 GB RAM.
The detailed routing results are verified by design rule checking in Cadence Innovus Implementation Systems 15.2 [20].

## Slide 23: EXPERIMENTS

## Slide 24: EXPERIMENTS

## Slide 25: EXPERIMENTS