## Slide 1: Power and Timing Optimization Using Multibit Flip-Flop
ICCAD 2025 Problem B

## Slide 2: Introduction
To develop a banking and debanking algorithm that produces a placement result optimized for timing, power, and area.

## Slide 3: Contest Objective
2025:
2024:

## Slide 4: Constraints
All instances must be placed on-site and within the die region.
No overlap
Must satisfy utilization rate of each bin
Banking / Debanking Criteria :
  All D pin and Q pin connections need to remain functionally equivalent after banking / debanking, and all CLK pins need to remain connected to the same clock net.
  If there is any design for testability (DFT) scan chain connection on scan-input (SI) or scan-output (SO) pins of the lower / higher-bit flip-flops, the banking / debanking process should honor the scan chain connection.

## Slide 5: Problem Formulation and Input/Output Format
Given:
  1.Weight factors for cost metrics (i.e. 𝛼, 𝛽, and 𝛾 )
  2.Timing slack and delay information
  3.Power information
  4.Area information
  5. Flip-Flop Library Cells
  6.Cell placement result with flip-flop cells ( LEF/DEF format )

## Slide 6: Problem Formulation and Input/Output Format
Output:
  A list of pin mapping between each input flip-flop pins and the output flip-flop pins
  A flip-flop placement solution (LEF/DEF format )

## Slide 7
Sample input: Sample output:

## Slide 8: Slack

## Slide 9: Score Function
TNS, Power, Area are reported using the command report_qor , report_power , report_qor from Fusion Compiler.
CPU Cores: You have 8 CPU cores available for your program.
Time Limit: The evaluation machine is limited to 60 minutes for each test case. The hidden cases will be in the same scale as public cases.